Transfer Protocol(TP) Packet Format and Details :-
TP(Transfer Protocol) has basically 3 modules inside it:
    1. VOC 2. TP and 3. IC

TP Module Packet Format:-
We are now going to discuss TP layer packet format.
TP packet is combination of TP header and message as shown in below fig:

TP Voice/Data Header
Data

TP Header	DATA(MSG)

TP Packet Format

TP layer adds TP Header to Actual Data. This TP header may be Voice Header or Data Header both contains useful information like message type I.e it is voice msg or data msg, source id, sequence number and length of message as shown below:

TP Voice Header:

4 bits
4 bits
12 bits
12 bits

Msg Length	Seq. No	Source Id	Message Type

TP Voice Header

Message Type : This 4 bits filed inform that message is DATA (0) or VOICE (1).
Source Id : This is also 4 bits field and contains the source id.
Sequence No : This 12 bit filed contains the sequence of Voice msg
Message Length : This field contains length of message. It also has 12 bit to store length.
TP Data Header :

4 bits
4 bits
12 bits
12 bits
16 bits

Checksum	Msg Len	Dest. Id	Src. Id	Msg Type

TP Data Header

Message Type :This 4 bits filed inform that message is DATA (0) or VOICE (1).
Source Id :This is also 4 bits field and contains the source id.
Destination Id :This is again 4 bits filed for destination id.
Message Length :This field contains length of message. It also has 12 bit to store length.
Checksum :This is for error detection.

IC Module Packet Format:-

Once TP header is added to data IC layer will receive that packet from TP layer and adds IC header and than final packet will be send to the counter side of this.

IC Packet Format is as shown below:

2 bits
2 bits

Dst. Id	Src. Id

IC Header

Source Id :- This 2 bits field contains Source Id .
Destination Id :- This is also 2 bits field and contains Destination Id.

Data packet with TP and IC header is going to be our final packet which looks as shown below:

IC Header	TP Header	Data